## Slide 1
Behzad Khajavi
Optical Engineer
Bio-Imaging Resource Center
The Rockefeller University
Fundamentals of Microscopy Course
Light Properties and Optical Principles

## Slide 2
Definitions
Electromagnetic fields and spectrum
EM field propagation (reflection, refraction)
EM field interference and diffraction
Manipulation of light rays
Building a basic microscope
Imaging, resolution, numerical aperture
Outline

## Slide 3
Optics: branch of Physics that studies the behavior and properties of light, its generation, propagation, interaction with matter, and detection.
Light: electromagnetic radiation that can be detected by the human eye; shows both wave and particle characteristics (visible EM).
Photon: the smallest discrete amount or quantum of electromagnetic radiation; has zero (rest) mass and travels at c = 299,792,458 m/s.
Definition
Quantum Optics
Electromagnetic Optics
Wave Optics
Ray Optics
Classical Optics
Photonics: science and technology of generating, controlling, and detecting photons (i.e., “particles” of light).
Biophotonics: optics with an emphasis on interaction of light with biological tissues
Biomedical Optics: design and application of advanced optical techniques to solve problems in medicine and biology

## Slide 4
Rectilinear propagation of light rays
Law of reflection,
(Euclid ~ 300 BC)
shortest path,
(Hero’s principle ~100 A.D.)
law of refraction,
dates to Ptolemy (~170 A.D.)
Basis of geometrical optics

## Slide 5
Electric field
stationary electric charge ,
at distance
in vacuum ()
(vacuum electric permittivity)
Magnetic field
wire carrying current I,
at position
in vacuum ()
(vacuum magnetic permeability)
Electric and magnetic fields

## Slide 6
Vector Wave Equation
(second-order linear PDE)
speed of light in vacuum
speed of light in medium
refractive index
Maxwell’s differential equations (in vacuum)
(linear, first-order partial differential equations (PDEs) in terms of field)
: Guass’s law (electric field)
: Guass’s law (Magnetic field)
: Faraday’s law
: Ampere’s law
Electromagnetic fields
(in vacuum)
c = 299,792,458 m/s

## Slide 7
https://w.wiki/Hzx3
c = 299,792,458 m/s
Electromagnetic spectrum

## Slide 8
human eye cone sensitivity curve
Electromagnetic spectrum

## Slide 9
EM wave is a transverse wave. Electric field vector oscillations determines the polarization:
Linear, Circular, Elliptical
EM field - Polarization
0  /2
0

/2
RCP
LCP
LP

## Slide 10
EM field - propagation
https://commons.wikimedia.org/wiki/File:Internal-reflection.gif
Reflection
https://en.wikipedia.org/wiki/Refraction
Refraction
n: Refractive index
is the parameter with which light slows down while propagating in a medium.
The ration speed of light in vacuum with respect to medium.
In vacuum:
In medium: , n>1
Refraction: Snell’s law
Reflection
http://hyperphysics.phy-astr.gsu.edu/hbase/phyopt/reflectcon.html#c1

## Slide 11
physics.thick.jp
Polarization effect in Reflection and Refraction
EM field - propagation
Refraction simulation
Polarizing BS in microscopes
Fresnel equations

## Slide 12
https://en.wikipedia.org/wiki/Reflection_(physics)#Laws_of_reflection
In vacuum:
In medium:
(function of source)
(Energy of light photon)
The color that our eyes perceive: Energy frequency
Refractive index, is a function of the wavelength
Material | n
air | 1
water | 1.33
PBS | 1.37
Immersion oil | 1.52
glass | 1.46 - 1.8
Refractive Index and Total Internal Reflection
EM field - propagation
Refractive index of most biological specimen is around 1.4

## Slide 13
Coherent light: well-defined relationship in phase at different points in space (wavelength dependent)
Generates constructive and destructive interference- useful for looking at path-length differences and moving light-scatterers
EM field - Coherence and Interference
Constructive Interference
Destructive Interference
http://study.com/cimages/multimages/16/

## Slide 14
https://evidentscientific.com/en/microscope-resource/knowledge-hub/lightandcolor/interference
For small
double slit interference of sunlight
EM field - Interference
Interference and Young’s double slit experiment

## Slide 15
Superposition of many interferences from an aperture (wavelength dependent)
MATLAB app
dispersion prisms separate wavelengths through refraction (top)
diffraction gratings separates wavelengths through diffraction (bottom)
EdmundOptics
[Most accurate approximation]
Rayleigh-Sommerfeld
Fresnel
Fraunhofer
[Least accurate approximation].
EM field - Diffraction
Double slit simulation
Notes: Demo gratings and laser pointers?

## Slide 16
Light Interaction with Matter
Photoelectric absorption
Scattering
(Compton, Rayleigh,…)
Pair Production
https://radiologykey.com/4-radiation-interactions-with-tissue/
Longer Wavelength : Rayleigh scattering

## Slide 17
C Dunsby and P M W French 2003 J. Phys. D: Appl. Phys. 36 R207
Light Interaction with Matter
EM wave (in material)
https://emanim.szialab.org/index.html
absorption
absorption + scattering
Light Propagation in Tissue

## Slide 18
light ray manipulation
Refraction, Reflection, Image formation, (De)Magnification

## Slide 19
light ray manipulation
Ray diagram for a converging lens
Rays parallel to symmetry axis (optical axis) get focused (focal point).
Rays crossing the center point of the lens are not refracted.
Rays crossing the focal point, refract parallel to the optical axis.

## Slide 20
4f system, separation = f1 + f2
Telecentric lens
www.thepulsar.be
light ray manipulation – 4f system, telescopes, telecentric scan, etc.

## Slide 21
https://www.schoolphysics.co.uk/
https://physics.stackexchange.com/
light ray manipulation – building microscope

## Slide 22
https://micro.magnet.fsu.edu/
light ray manipulation – building microscope

## Slide 23
light ray manipulation – Objectives
Objectives come in various designs.
Dry, water, oil, NA, working distance, aberrations, etc.

## Slide 24
Douglas B. Murphy Michael W. Davidson, Fundamentals of Light Microscopy..
https://phys.libretexts.org/
Resolution and NA dependence
finer periodic structures leaves the sample at a higher angle.
Diffraction gratings Demo
The angle of spreading (θ) is
inversely proportional to the size of the particles

## Slide 25
https://www.teledynevisionsolutions.com/learn/learning-center/scientific-imaging/resolution-and-numerical-aperture/
The numerical aperture of a microscope objective is a measure of its ability to gather light and resolve fine specimen detail at a fixed object distance.
Resolution and NA dependence
Numerical Aperture:
n: refractive index
: is the half-angle of the maximum cone of light that can enter or exit the lens

## Slide 26
https://bioimagebook.github.io/
The image (g) = the convolution of the object ( f) and the PSF (h)
PSF: Point Spread Function (how a point-like object appears)
https://svi.n
Abbe Lateral Res
Abbe Axial Res
Image formation, PSF, and Resolution

## Slide 27
https://zeiss-campus.magnet.fsu.edu/
Lateral Res
Axial Res
If :
Lateral Res (Abbe formula)
Resolution and NA dependence
In epi FL microscopes the objective acts as the condenser:
Lateral resolution: only objective NA

## Slide 28
https://bioimagebook.github.io/
The Rayleigh criterion : the minimum resolvable detail.
“The first diffraction minimum of the image of one source point coincides with the maximum of another.”
Rayleigh Lateral Res
Diffraction limited resolution
Resolution Limit Imposed by Wave Nature of Light

## Slide 29
https://zeiss-campus.magnet.fsu.edu/
light ray manipulation – Kӧhler illumination
www.teledynevisionsolutions.com/
Uniform illumination using several lenses

## Slide 30
Illumination
Sources
Detectors
Microscope main components
Data Acquisition
Components
Optical Components

## Slide 31
Lamps
Broad spectral excitation
LEDs
Cheap, Long-lasting, Poor spectral purity, Hard to focus into fibers, Portable systems
Laser Diodes
High-power, Better coherence, Stable, Easy to couple w/ fibers, Delicate – easy to burn down, More expensive
Laser Systems
Desired bandwidth, wavelength, stability, frequency, high coherency, Most expensive
Lowest coherency
Highest coherency
Microscope main components – Illumination sources

## Slide 32
Microscope main components - Optics
Mirrors:
Broadband dielectric, gold, cylindrical,
Concave,
Beamsplitters: X/Y (50/50), Dichromatic, Polarizing,…
Filters: Intensity (ND), bandpass, long/short pass, polarization, …
Lenses:
Aspheric, Achromatic,
Convex,
Concave,
Doublet,
Powell,
Cylindrical,
…

## Slide 33
Photodiodes
(PN junction diode in reverse bias) cheap, high speed, moderate sensitivity
Microscope main components - Detectors
Avalanche Photo Diodes (APD) high gain/sensitivity, higher cost, more delicate
Photomultiplier tubes (PMT) very high gain/sensitivity, require high voltage, prone to damage, limited near-IR reach (< 850 nm)

## Slide 34
Charge coupled devices (CCD)
Analog
Linked capacitors transfer charges
Cheap
Microscope main components - Detectors
Complementary metal–oxide–semiconductor (CMOS)
Digital
High speed
Low sensitivity
sCMOS (Scientific CMOS)
Very low noise

## Slide 35
Microscope main components - DAQ components
Analog to Digital Card (Digitizer)
Converts the analog signal pulses to digital ones
Transfers data …
High Speed Data
Storage drive
Up to several GB/s data transfer speed
Camera (Detector array)
Frame Grabber
Converts the signal pulses from camera (detector array) to digital ones
Transfers data …

## Slide 36
Multifunction I/O Modules, BNC cables, fibers, etc.
Microscope main components - DAQ components

## Slide 37
Microscope main components - Software
Software (Acquisition & Processing)
1
2
N
2
1
M
Camera frame width: N
Camera frame height: M
Processing procedure could be composed of: Averaging, filtering/Noise removing methods, deconvolution, etc.
(Explained in second session of the course)
1
2
N
Signal data stream
Single detector
Detector array

## Slide 38
openspim.org
mesospim.org
aicjanelia.org/mosaic
Examples of noncommercial microscopes

## Slide 39
Thanks
Bio Imaging Resource Center team
Alison North,
Ivan Rey Suarez,
Tao Tong,
Ved Sharma,
Maria Belen Harreguy Alfonso,
Priyam Banerjee,